ABI CARPET LOGOMAT

| SPECIFICATIONS |  |
| --- | --- |
| Yarn: | Continuous filament PET yarn with 50% post-consumer recycled content |
| Weight: | 900 gr / m2 |
| Pile height: | 11mm |
| Static control: | ISO 6356 (2012) Determination of the static electrical propensity Walking test: -0.3 KVolts Satisfies IBM test requirements |
| Total weight: | 2.90 kg / m2 |
| Primary backing: | Freudenberg LutradurTM Polyester Spun bound Non-woven Fabric 130 gr / m2 |
| Rubber backing: | 100% Nitrile EXSTM rubber for maximum oil resistance, weight reduction and flexibility. Compression molded with reinforced borders on all four sides Border Thickness: 2.5 mm Body Thickness: 1.5 mm |
| Border width: | 2 cm |
| Size variance: | +/- 2% |
| Flammability: | Passes BS 4790 (1987) determination of the flammability of textile floor coverings: Low radius of effects of ignition. |

| STANDARD SIZES (cm) |
| --- |
| 60 x 85 | 85 x 300 | 115 x 250 | 150 x 250 |
| 75 x 85 | 115 x 180 | 115 x 300 | 150 x 300 |
| 85 x 115 | 115 x 200 | 150 x 200 | 200 x 200 |
| 85 x 150 | 115 x 240 | 150 x 240 | 200 x 300 |
| Special shapes and sizes are also available. Maximum size: 200 x 550 cm. Ask our sales team for the options. |

| COLOURS |  |
| --- | --- |
| 66 different colours |